## Slide 1
CONCLUSION & FUTURE WORK
VEHICLE DETECTION
IMAGE PROCESSING
VISTA – COMPUTER VISION INNOVATIONS FOR SAFE TRAFFIC
VEHICLE ORIGIN DETECTION USING LICENSE PLATE RECOGNITION
OPTIMIZATION AND SPEED UP
Overall objectives:
  Strengthening of technology transfer and commercialization capacities of partner HEIs
  Transfer of existing computer vision applications from HEIs to SMEs
  Developing new traffic- and transportation-related computer vision applications with commercial potential in collaboration with SMEs in the automotive industry sector
Measurement of road traffic parameters based on computer vision
ACKNOWLEDGEMENTS
Basic work flow of vehicle detection consists of:
Original image (a) down sampled and blurred (b)
Creation of background image model and comparison of background image model and current image (c)
Pixel clusterization and grouping (d)
VEHICLE TRACKING AND COUNTING
In the proposed system, spatio-temporal tracking of objects in a scene is used for filtering
Every currently tracked object in the scene is compared with each cluster detected in the current image
When a vehicle passes through marker and a hit is detected, counter for that marker is incremented
University of Zagreb, Faculty of Transport and Traffic Sciences
www.unizg.hr, www.fpz.unizg.hr, its.fpz.hr
Faculty of Electrical Engineering and Computing (UNIZG-FER) leading institution
  Project leader: prof. dr. sc. Sven Lončarić
Faculty of Transport and Traffic Sciences (UNIZG-FTTS) partner institution
  Local project leader: prof. dr. sc. Hrvoje Gold
Project start date / duration: 30.03.2013. / 24 months
Project budget: 685,265.45 €
This work has been supported by the IPA2007/HR/16IPO/001-040514 project “VISTA - Computer Vision Innovations for Safe Traffic” which is co-financed by the European Union from the European Regional and Development Fund.
a)
b)
c)
d)
Kristian Kovačić | Edouard Ivanjko | Niko Jelušić | Hrvoje Gold
kkovacic@fpz.hr | eivanjko@fpz.hr | njelusic@fpz.hr | hgold@fpz.hr
Development of:
  Detection of road-side vegetation for traffic infrastructure maintenance
  Surround-view parking visualization
  Traffic sign detection and recognition
  Lane detection and recognition
  Lane departure and collision warning
  Automatic headlight detection
  Driver mental state recognition
Approach |  | Vehicle count |  | 
 |  | Total | Left | Right
Overlap check | Hits | 126 | 65 | 61
 | FP / FN | 0 / 6 | 0 / 5 | 0 / 1
 | Accuracy [%] | 95,6 | 92,9 | 98,4
Trajectory check | Hits | 129 | 68 | 61
 | FP / FN | 1 / 4 | 0 / 3 | 1 / 1
 | Accuracy [%] | 96,2 | 95,8 | 96,8
Groundtruth |  | 132 | 70 | 62
1. Video input
2. Using contours for vehicle detection
3. Variable image size for License Plate Recognition
Country | Number of vehicles | Percentage [%]
Germany | 166 | 31.2
Poland | 88 | 16.5
Austria | 83 | 15.6
Czech Republic | 72 | 13.5
Croatia | 47 | 8.8
Others | 76 | 14.4
4. Vehicle country of origin distribution table
Developed system uses only one camera to detect and track vehicles in real time on a road with multiple lanes
First testing results are promising with vehicle detection accuracy of over 95%
Future work consists of developing a multiple object tracking system which would perform vehicle classification and therefore separate vehicles by their type, compute origin-destination matrices by identifying each individual vehicle and tracking it through monitored road traffic network
Computed error between estimated (EKF) and real trajectory
Counted vehicles in a video footage from Croatian highway near Zagreb
Execution time needed for processing of a single image
Architecture of optimized application
22ND SUMMER SCHOOL ON IMAGE PROCESSING – SSIP 2014, ZAGREB, CROATIA