## Slide 1: Real time vehicle trajectory estimation on multiple lanes
Kristian Kovačić, Edouard Ivanjko, Hrvoje Gold
kristian.kovacic@fpz.hr

## Slide 2
University of Zagreb
Faculty of Transport and Traffic Sciences
Introduction
Vehicle detection
Vehicle trajectory estimation
Vehicle detection speed up
Experimental results
Conclusion and future work
Outline

## Slide 3
Introduction
New ITS based traffic control approaches need real time data
Video camera is more and more used for traffic parameters measurement
  Vehicle detection for flow and velocity measurement
  Origin-Destination (OD) matrices
  License plate recognition, etc.
Problem
  Tracking vehicles on multiple lanes simultaneously with only one camera
    Commercial versions need one camera per lane

## Slide 4
Vehicle detection
Image import
  IP camera, video file
Preprocessing algorithm
  Noise reduction
  Gaussian filter with 5x5 matrix

## Slide 5
Vehicle detection
Background substraction method
  (a) Creation of background image model
  (b) Detection of foreground objects

## Slide 6
Vehicle detection
Object clustering method
  Check if adjacent pixels exist and combine them into cluster
  If cluster area A ≤ threshold, remove cluster
Object tracking method
  Compare all objects in the new frame with objects in the previous frame and combine only those with max w
1
2
3
Vehicle trajectory estimation

## Slide 7
Vehicle trajectory estimation
Postprocessing object location
  Extended Kalman Filter
  Histogram for computing average values of position (x, y), velocity (v), acceleration (a), direction (ϕ), angular velocity (ω) based on EKF output
  Setting initial values of state vector x by histogram
    Measurement vector
    State vector

## Slide 8
Vehicle detection
Speed up
Optimization approach
  Executing algorithms on GPU as much as possible
  Adding support for CPU SIMD instructions to algorithms which are incapable to run on GPU
  Performing computations using multiple threads
    Parallelization of image processing algorithms

## Slide 9
Experimental results
Vehicle detection accuracy
Approach |  | Vehicle count per lane |  | 
 |  | Total | Left | Right
Overlap check | Hits | 126 | 65 | 61
 | FP / FN | 0 / 6 | 0 / 5 | 0 / 1
 | Accuracy | 95,6% | 92,9% | 98,4%
Trajectory check | Hits | 129 | 68 | 61
 | FP / FN | 1 / 4 | 0 / 3 | 1 / 1
 | Accuracy | 96,2% | 95,8% | 96,8%
True vehicle count |  | 132 | 70 | 62
Vehicle counting approaches
  Check if vehicle bounding box / trajectory is overlapping with one of virtual markers

## Slide 10
Experimental results
Vehicle trajectory estimation accuracy
Simulation of 3D road traffic scene with known parameters
  Synthetic environment designed in Autodesk 3ds Max
  Noise added to measured trajectory

## Slide 11
Experimental results
Execution time
Execution time distribution per image processing component
Overall execution time of application

## Slide 12
Experimental results
Arised problems
Overlapping vehicles cause false positive and false negative detections
Environment conditions (sun reflection, rapid lighting changes), camera vibrations caused by strong wind or passing of large vehicles

## Slide 13
Conclusion
Future work
One camera can be used for multiple lanes
  Vehicle detection and tracking
Vehicle detection and trajectory estimation in real time
  Measuring traffic flow
First results promising
  Vehicle counting accuracy over 95%
Future work
  Vehicle classification (bicyclist, car, truck)
  Possible to use one camera per one road traffic network node
  Computation of origin-destination matrix of a large road traffic network using license plate recognition

## Slide 14
University of Zagreb
Faculty of Transport and Traffic Sciences
Acknowledgment
This research has been partially supported by
European Union from the European Regional Development Fund by the project IPA2007/HR/16IPO/001-040514 ”VISTA - Computer Vision Innovations for Safe Traffic”
  Leading institution University of Zagreb, Faculty of electrical engineering and computing
EU COST action TU1102 - “Towards Autonomic Road Transport Support Systems”

## Slide 15: Real time vehicle trajectory estimation on multiple lanes
Kristian Kovačić, Edouard Ivanjko, Hrvoje Gold
kristian.kovacic@fpz.hr